## Slide 1: IDENTITY NUMBERS
BY
A.M.VILLAVAN
M.TECH(COS)

## Slide 2: RFID
Acronymn: Radio Frequency Identification Device
RFID is a technology, whose origins are found in the WWII era, that incorporates electromagnetic or electrostatic coupling in the RF portion of the EM spectrum to uniquely identify an object, animal or person.
Holds a small amount of unique data – a serial number or other unique attributes of the item
The data can be read from a distance – no contact or even line of sight necessary

## Slide 3: CONT…
Radio Frequency Identification
The use of radio frequency tags to identify real objects.
Assign IDs to objects
Link the ID to additional information about the object
Link the ID to complementary info
Find similar objects

## Slide 4: IDENTIFICATION EXAMPLES
Bar Codes
License Plates
Social Security Numbers
Student ID
Serial Numbers
Car Keys

## Slide 5: HOW DOES RF WORKS
3 Components
  Transceiver – Tag Reader
  Transponder – RFID tag
  Antenna

## Slide 6
Objects equipped with RFID tag
  Tag contains transponder with digital memory chip.
Interrogator: an antenna packaged with transceiver and decoder.
  emits signal activating tag.
Reader detects activation signal, decodes the data on the tag’s silicon chip.
Data passed to host computer.

## Slide 7: RFID STANDARDS
Tracking Animals
  ISO 11784 – Specifies the structure of the ID code
  ISO 11785 – Specifies how transponder is activated
  ISO 14223/1 – Specifies RF code for advanced transponders
Credit Cards
  ISO 15693 – Specifies modulation and coding schemes
Passports and proximity cards
  ISO 14443 – Specifies modulation and coding schemes
General Frequency bands
  ISO 18000 series

## Slide 8: FREQ RANGE OF RFID STANDARDS
ISO 18000-2
  <135 KHz
ISO 18000-3
  13.56 MHZ
ISO 18000-4
  2.45 GHz
ISO 18000-6
  860-960 MHz
ISO 18000-7
  433 MHZ (active)

## Slide 9: ACTIVE RFID TAG
Battery Powered tags
  Have much greater range – 100m
  Hold much more information – Kbytes
  Can integrate sensing technology
    Temperature, GPS
  Can signal at defined time
  Multiple tags can be recorded/read at once
Used for higher value items
  Shipping containers
  Electronic assets
Cost between $20 and $40 per item
Life between 2 – 4 years

## Slide 10: PASSIVE RFID TAG
“Traditional” tags used in retail security applications
  Tag contains an antenna, and a small chip that stores a small amount of data
  Tag can be programmed at manufacture or on installation
  Tag is powered by the high power electromagnetic field generated by the antennas – usually in doorways
  The field allows the chip/antenna to reflect back an extremely weak signal containing the data
  Collision Detection – recognition of multiple tags in the read range – is employed to separately read the individual tags

## Slide 11: APPLICATIONS
Tracking Books in Libraries
Passports (US passports recently)
AmEx Blue credit card
Prison inmates (embedded)

## Slide 12: CONT…..
For toll booths (or any “pay for entry” system)
Airport Baggage ID
Car keys, wireless entry and ignition
Animals
Hospital Patients
  Instant history tracking

## Slide 13: DISADVANTAGES
Cost
  Transceiver ~ $1000
  RFID Tags $0.20 each
  Not competitive with cost of barcode
UHF signals problematic near metal and water
Reader Collisions
  Can be overcome using TDMA
Tag Collisions
  Required some engineering of tag transmit timing
Security Concerns

## Slide 14: CONCLUSION
RFID technology is rapidly becoming more standardized, but problems do still exist
The number of adopters of RFID technology is growing
Regulation and education is necessary to quell some of the fears regarding RFID technology and it’s implications

## Slide 15
THANK YOU